## Slide 1: Implementing 5G Down Link Power Control Using Reinforcement Learning via NetSim-Python Interfacing
Applicable Release: NetSim v14.0.34 or higher
Applicable Version(s): NetSim Standard and NetSim Pro
Project download link: https://github.com/NetSim-TETCOS/DBR_IN_UWAN_v14/archive/refs/heads/main.zip
The URL has the configuration files (scenario, settings, and other related files) of the examples discussed in this analysis for users to import and run in NetSim

## Slide 2: How to run the RL simulation ?
Download the project from Github link provided in slide 1.
Follow the instructions provided in the following link to setup the project in NetSim
  https://support.tetcos.com/support/solutions/articles/14000128666-downloading-and-setting-up-netsim-file-exchange-projects
For the RL simulation, we first need to run NetSim using the command line interface(CLI)
Open the Run menu with Windows Key + R, then type "cmd." Press "Enter" to open Command Prompt
Note the application path. Application path is the current workspace location of the NetSim that you want to run. The default application path will be something like "C:\Users\PC\Documents\NetSim\Workspaces\\<Your default workspace>\bin_x64" for 64-bit.
Change the directory to the application path using the following command
>cd \<app path>

## Slide 3: How to run the RL simulation ?
Type the following in the command prompt
FOR /L %i IN (1,1,<NUM_EPISODES>) DO NetSimCore.exe\<space>-iopath\<space>\<io path>\<space>-license\<space>5053@\<Server IP Address>
  \<iopath> is the path to the current scenario which needs to be run, which in this case is “RL_based_Power_Control_Sample”
  \<Server IP Address> is the ip address of the system where NetSim license server is running.
  <NUM_EPISODES> is the number of episodes the simulation will run for; default value is 500
Now, open another command prompt window and change the directory to where the python file “RL_Power_Control” is saved
Type python <filename>, in this case, filename is “RL_Power_Control” and hit enter to run the python file
The python script will ask for the number of episodes as input, enter the default value, 500 and hit enter to start the simulation

## Slide 4: Power Control: Introduction
Due to the broadcast nature of wireless communication, signals interfere with each other.
Interference can degrade the performance of the 5G RAN
DL power control can be used to mitigate interference, ensure spectral reuse and improve user experience
However, direct application to practical systems is impaired by the dependency on various simplifying assumptions
  Knowledge of channel gains from all BSs to all UEs,
  Full buffer traffic,
  Knowledge of user positions, number of users, resources allocated to each user etc.
In this project, we use reinforcement learning (RL) for downlink (DL) power control to mitigate interference, boost SINR and maximize sum throughput

## Slide 5: Reinforcement Learning: Tabular
Environment: The 5G cellular network
Agent: Logical nodes at each gNB implementing the RL algorithm
State: Vector of received SINRs at the UEs
Action: Power Control i.e., power-up, power-down, power-hold
  A control of ∆P applied to all gNBs
  Agent applies power control every 3 slots
Reward function:
  R1: Sum throughput
  R2: Sum log throughput
  Throughput averaged every 3 slots i.e., time between two consecutive actions

## Slide 6: NetSim Model
3gNBs and 6 UEs
  UEs download data from a remote server
Channel model
  Pathloss: Log distance with 3
  Rayleigh fading
BS (gNB) determines the rate based on 3GPP standards
  Maps received SINR to an MCS, per 3GPP table ____
Antenna counts at gNBs and UEs: 1Tx, 1 Rx
No error
Full buffer traffic. Packet size 1500 B.
  In NetSim, packets are grouped in a TB. The TB is split into CB. Then CBs are grouped into CBGs which are transmitted over the air.

## Slide 7: SINR and Rate
Channel attenuation: Pathloss: Log distance with , Rayleigh fading
SINR formula
Spectral Efficiency (SE) in bits per second per Hz
Look up the 3GPP table ___ mapping SE to MCS.

## Slide 8: Tabular Q Learning: Algorithm
To avoid the state and action space explosion, both state and action spaces are discretized
The state space is discretized based on SINR
  Bucket 1: < -5 dB
  Bucket 2: 5 dB to +3 dB
  Bucket 3: +3 dB to +11 dB
  Bucket 4: 11 dB
Action space is discretized based on power up/down
  Transmit power limits: [27, 46] dBm
Number of entries in Q-table
  States: = 4096
  Actions: = 125
  Total: 600k

## Slide 9: NetSim Python Interfacing
1. Introduction to Python C Socket Interfacing:
  Python facilitates seamless integration with C for socket programming tasks.
  Python uses the socket module to interact with C side functions.
2. Python Code:
  Python creates a client socket in the host machine and connects with the C side server
  Key functions include:
def NETSIM_interface(gNB_powers):
  Sends the gNB powers to NetSim with a header
  Receives acknowledgement integer value from NetSim
  Sends a request value to NetSim to receive the updated SINR values and the reward
  Receives the next state and the reward from NetSim

## Slide 10: NetSim Python Interfacing (Contd.)
C side code
  Key functions include:
void init_waiting_struct_socket1() : Initializes the Winsock library and calls the listenForPython() function bool listenForPython() : Resolves the server address and port Creates a socket for connecting to the server Sets up the TCP listening socket Waits for client socket connection void handle_Send_Receive(struct SINR_Values_Reward* Param1, struct gNB_Powers* Param2)

## Slide 11: NetSim Python Interfacing (Contd.)
C side code
  Key functions include:
void handle_Send_Receive(struct SINR_Values_Reward* Param1, struct gNB_Powers* Param2) Receives the message type from Python If message type is to “receive gNB powers”, receives the powers from Python and sends back an acknowledgement message If message type is to “send SINRS and rewards”, sends back the state and reward back to Python using the send_SINRS_Rewards_at_Time_Step() function void send_SINRS_Rewards_at_Time_Step() : sends the list of updated SINRs and the sum throughput received from the LTENR project in NetSim back to python

## Slide 12: Parameters
Parameter | Value
Bandwidth | 50 MHz
Transmit Power | 40 dB
Noise Power | -96.38 dB
Path-loss exponent | 3
Hyper parameter | Values
 | 0.9
 | 0.3
 | 0.25
Hyper parameter | Values
 | 0.9
 | 0.3
 | 0.25

## Slide 13: Performance Evaluation: UE Throughputs

## Slide 14: Results